CSTE3028 998 Flat top piston range  (+0.020”, 0.040”, 0.060”, 0.080”, 0.100”)   -  Fitting information                  October 2015

This piston set can be used with both floating and press fit type applications/con rods. The only difference is that when used with the press fit con rod type, the circlips are not used. The press fit con rod uses the same diameter wrist pin as that of the floating pin type.

These pistons are manufactured from a far superior aluminium than most high performance pistons. They contain a much higher silicone content and advance heat treatments which creates a more stable piston. This dramatically reduces expansion under combustion/running conditions. Consequently lower piston to bore clearances are required. They are manufactured for race use so will give correct piston to bore clearance on the relevant bore size. Suggested finished honed bore to piston clearances are as follows -

Road/fast road         -  0.0015” to 0.0017” (0.0381mm to 0.0432mm)

Sports/super sports  -  0.0018”  to 0 0.002” (0.0457mm to 0.0508mm)

Race                        -  0.0022” to 0.0025”  (0.0559mm to 0.0635mm)

IMPORTANT - Because the standard available gaskets over-hang the bore on the +0.080” and and +0.100”  bore sizes, make sure the piston crowns are at least 0.010” below the block face when at top dead centre. For blocks that have already been re-faced sufficiently so it is either already flush with the piston crowns at top dead centre or the pistons actually protrude from the bore – either machine the piston crowns to give the desired crown to block face clearance, or machine a chamfer on to the top edge of the piston crown.

The top and second compression piston rings should be correctly gapped to give 0.004” per 1.0” of bore diameter. i.e. for a +0.060” bore this will be 2.543” + 0.060” = 2.603” bore diameter. Ring gaps will then be 0.004” x 2.603” = 0.010”. Some ring sets come supplied with large ring gaps, up to 0.020”. This is not a problem. The oil control rings should just be assembled to the piston as they are because the assembly is designed to work at it's compressed in-situ form. This is not measurable with the piston out of the bore.

Piston ring orientation -

Top ring – Matt light-grey moly-coated face, fit with letter/numbers facing piston top

Second ring – Slate grey coloured ring, fit with letter/numbers facing piston top

Oil Control rings – Universal, fit expander first then lower rail then upper rail.

Ring end gaps should be fitted so there are no over-laps between the rings. Fit piston to bore with top ring end gap at rear of piston, 90 degrees to wrist pin axis. Position second ring with end gap at front of piston, 90 degrees to wrist pin axis, 180 degrees from top ring end gap. Position oil control expander ring with gap directly below 2nd ring gap, then bottom rail with end gap 120 degrees clockwise to this, and top rail gap at 120 degrees clockwise from that.